## Slide 1: Process Control
Topics for Project 2
Brad Nelson
Modified Bill Stefanuk W2015

## Slide 2: Project 2…
DC Motors (travel)
Optical Encoders
(travel feedback)
RC Servo Motor (camera tilt)
Stepper Motor (camera pan)
Executive (supervisory) control

## Slide 3: Topics:
Pointing the camera
Differential drive & steering
PM DC motor speed control

## Slide 4: Topics:
Pointing the camera
Differential drive & steering
PM DC motor speed control

## Slide 5: Project 2 camera pointing…
DC Motors (travel)
Optical Encoders
(travel feedback)
RC Servo Motor (camera tilt)
Stepper Motor (camera pan)
Home position for the Camera

## Slide 6: Homing the Camera…
Relative vs Absolute
RC servo is absolute position device
  Duty cycle command moves servo to a specified (absolute) position
Stepper motor is relative position device
  Phase pattern changes move the motor relative to its current position
Why do we care?
  You need to do something special to know where the stepper motor is pointing the camera.
Homing
  Process of taking the camera to a known position so relative stepper motor moves point the camera in a known direction

## Slide 7: To Home the Camera…
Set the tilt (RC servo) to point the camera straight ahead
Run the stepper motor in 1 direction until the limit switch in that direction is hit.
Stop stepping, zero out a position counter variable and start stepping in the other direction.
Continue stepping and counting steps until the other limit switch is hit.
Stop stepping, reverse direction and command the stepper to return to the middle of its range.
Now the camera is “home”

## Slide 8: What could go wrong?
You have directions backwards and you’re running towards the wrong limit switch. (Solution: Check for both, and report an error if you hit the wrong one)
The switch is broken or disconnected and you never see it trip, or the motor doesn’t spin. (Solution: Timeout on hitting a limit switch. Error if it takes too long)

## Slide 9: Commands to point the camera…
Absolute and relative … you’ll need both
  … but relative is the more important for joystick control
RC servo = camera Tilt
  Tilt camera to specified angle
    T 0 -200 // tilt to angle of -20 degrees
    T 0 150 // tilt to angle + 15 degrees
  Tilt camera by specified angle
    T 1 50 // increase tilt by +5 degrees
    T 1 -50 // decrease tilt by -5 degrees
Stepper motor = camera Pan
    S 0 450
    S 1 -100

## Slide 10: Positioning the Servo…
1500 μs is centre
180° travel +/- 90 °
  100 μs = 10°
  Maximum CCW = 1500 – 900 = 600 μs
  Maximum CW = 1500 + 900 = 2400 μs
Graphics – www.ServoCity.com

## Slide 11: RC Servo Positioning…
What duration pulse will move it to the -45 degree position?
-90
Position (degrees)
0
+90
0.6
1.5
2.4
Pulse Time (ms)
-45
1.05
Your Turn!
Work out an expression relating output pulse time in μs to input angle in degrees
Brad Nelson - modified

## Slide 12: Converting to TCNT ticks…
To position the RC servo, you write a value to a timer register that represents TCNT ticks.
If your timer prescaler is 8, TCNT is counting µs directly …. so the formula we just worked out works directly.
If your timer prescaler is 32, TCNT is counting in 4 µs chunks … so the formula we just worked out needs a factor of 8/32 = ¼ to convert µs into TCNT ticks

## Slide 13: Topics:
Pointing the camera
Differential drive & steering
PM DC motor speed control

## Slide 14: Project 2 drive motor control…
DC Motors (travel)
Optical Encoders
(travel feedback)
RC Servo Motor (camera tilt)
Stepper Motor (camera pan)
Brad Nelson

## Slide 15: Steering by Differential Speed
Straight motion
- Both motors same speed and direction
Turning
- Slower motor on inside of turn
- Speed difference depends on the…
- radius of the turn
- time of the turn (or overall speed)
- distance between the wheels
Front
Brad Nelson – Session 10 – Speed and Position Control (2010)

## Slide 16: Control Speed and Track Distance…
Speed is…
  Number of encoder vanes per unit of time
  … or the reciprocal of the period of a single encoder vane
  Implement and tune a closed loop controller that maintains the desired encoder vane frequency
Distance is…
  Total number of encoder vanes seen
  While controlling speed, count the number of vanes seen to track distance travelled

## Slide 17: The Robot Driveline… Distance
Break-beam optical sensor
27 vane disk
Gearbox – 22.5:1
1 wheel rotation = π x 5.3 cm = 16.65 cm = 166.5 mm of travel
1 wheel rotation = 1 motor output shaft rotation = 22.5 encoder disk shaft rotations
1 wheel rotation = 22.5 x 27 = 607.5 encoder vanes
607.5 encoder vanes = 166.5 mm of travel
1 encoder vane = 166.5/607.5 = 0.2741 mm of travel
      1 encoder vane = 0.2741 mm of travel

## Slide 18: The Robot Driveline…Speed
Break-beam optical sensor
27 vane disk
Gearbox – 22.5:1
1 encoder vane = 0.2741 mm of travel
1 mm/s = 1/0.2741 encoder vanes/second = 3.648 encoder vanes/second
Period of 1 encoder vane = 0.2741 / (speed in mm/s)

## Slide 19: You’ll Need to Handle…
Travelling in a straight line at a specified constant speed for a specified distance
  Wheels travel same distance at same speed
Travelling along a circular path at a specified constant speed for a specified distance
  Wheels travel different distances at different speeds
Spinning on the spot by a specified number of degrees in a specified time
  Wheels travel same distance in opposite directions at the same speed
  (this is just a special case of 2 above)

## Slide 20: Steering by Differential Speed
W
R
ω (angular speed in rad/sec) is the same for each radius
where
ω = V / R (V is linear velocity and R is the turn radius)
and
e.g. For a turn radius R of 100 cm at a speed V of 30 cm/s with a wheel width W of 20 cm, the outer and inner wheels must go…
Router
Rinner
Brad Nelson – Session 10 – Speed and Position Control (2010)

## Slide 21: Differential Distance
W
R
θ (angular displacement in rad) is same for each radius
where
θ = d / R (d is linear distance and R is turn radius)
and
e.g. For a turn radius R of 100 cm and a specified turn of 90 deg, the outer and inner wheels must travel…
Router
Rinner
Brad Nelson – Session 10 – Speed and Position Control (2010)

## Slide 22: Differential Distance
For a 90 deg turn-on-the-spot
* assuming wheel spacing W is 20 cm
Brad Nelson – Session 10 – Speed and Position Control (2010)

## Slide 23: Topics:
Pointing the camera
Differential drive & steering
PM DC motor speed control

## Slide 24: Platform Speed Control
Encoder
PI control
PWM Motor Driver
DC Motor
Desired speed
Measured rate
Actual speed
LEFT WHEEL
Encoder
PI control
PWM Motor Driver
DC Motor
Desired speed
Measured rate
Actual speed
RIGHT WHEEL
Brad Nelson

## Slide 25: Consider a DC Motor control loop…
Software inside your HCS12

## Slide 26: On your board…
Control Law Calculation (Output Compare ISR)
Controller Output (PWM)
Feedback (Input Capture)
Where does the setpoint come from?

## Slide 27: What about direction?
You setup H-bridge control lines to set direction.
Controller is the same regardless of direction. Why?
ONLY CHANGE DIRECTION WHEN THE MOTOR IS STOPPED!!! Why?

## Slide 28: So you need to write…
Code to measure the speed of the motor (period of the encoder)
  Input Capture ISR for each motor
  Timer Overflow ISR to track wrapping of the 16-bit counter
Code to calculate the required PWM drive value given the difference between the setpoint and the measured speed
  Output Compare ISR to run the control law code on a regular timebase
Code to set the PWM output with the appropriate value determined by the control law
Code to pass a direction and setpoint speed to the motor control ISR and start the motor turning in the correct direction
Code to initialize all the required hardware (timer module, timer channels, PWM channels) and control variables

## Slide 29: Sampling Rate
The constant ∆t (or T) term is the sampling time
The sampling rate is 1/∆t or 1/T… the number of times per second the controller produces a new output value
The slower the sampling rate, the less responsive and stable the system. Limit to how much improvement from sampling faster.
Too slow sampling may miss crucial sensor changes and thus misinterpret the data (a side-effect of slow sampling called aliasing)

## Slide 30: PI controller
Controller Output = (P Gain * Speed Error) + (I Gain * Speed Error Integral)
Speed Error Integral = <Sum of all speed errors since the controller started>
I Gain = <integral gain term – you tune this>

## Slide 31: Remember… A simple LINEAR controller…
Error = desired motor speed – measured motor speed
Assumption! Feedback signal is a linear representation of motor speed

## Slide 32
Capture TCNT for two consecutive rising or falling edges
Calculate the difference as the encoder vane period
If TCLK is fast enough, can get great speed resolution
  Need the encoder period shorter than the servo period
Period Measurement

## Slide 33: But there’s a tiny problem …

## Slide 34: The problem (and solution)…
Encoder vane period is NOT linear to motor speed
It’s a reciprocal relationship. Period is inversely proportional to speed (a hyperbola).
Need vane frequency -- directly proportional
Solution:
  Linearize the period measurements to make them directly proportional by converting back to a frequency
Servo and Encoder Calcs - W2010 - WPS.xls

## Slide 35
Need to convert from engineering units (cm/s) to the internal values use by the controller (SREP)
Only when the setpoint changes
Every time the controller runs
Calculating the Error Term…

## Slide 36: Real-World Controller Issues…
Is the feedback data garbage? If so don’t run the control law
Limits on the valid range of outputs –PWM Duty Cycle register values
Reset Windup – if the output is already at the limit, stop integrating
Must be fast

## Slide 37: Let’s look a bit more closely at the calculations…
driveValue = (speedError * P_GAIN)
+ (speedErrorIntegral * I_GAIN);
driveValue = (unsigned char)((speedError * P_GAIN)
+ (speedErrorIntegral * I_GAIN));
What values might we want for P_GAIN and I_GAIN?
So what might their type declarations look like?
double P_GAIN, I_GAIN;
But we need a byte result for the PWM module!?
What’s wrong with this picture?

## Slide 38: A Sketch of a Control Law Function…
/* calculate error term */
speedError = (S32)setpoint - (S32)(FEEDBACK_SCALE_FACTOR/encoderVanePeriod);
/* check for stupid speed error - spurious interrupt,etc. - don't run controller if garbage */
if ((speedError < STUPID_SPEED_ERROR) && (speedError > -STUPID_SPEED_ERROR)) {
/* update integral term but only if drive is not on the rail */
if ((motorPWMvalue == MIN_DRIVE_VALUE) && (speedError > 0)) ||
((motorPWMvalue == MAX_DRIVE_VALUE) && (speedError < 0)) ||
((motorPWMvalue > MIN_DRIVE_VALUE) && (motorPWMvalue < MAX_DRIVE_VALUE))
SpeedErrorIntegral += speedError;
/* calculate the control law (NB: PI - no derivative term) */
/* This is ALL integer math. */
driveValue = ((speedError * P_GAIN)
+ (speedErrorIntegral * I_GAIN)) / GAIN_DIVISOR;
/* limit the controller output to range of PWM */
if (driveValue > MAX_DRIVE_VALUE)
driveValue = MAX_DRIVE_VALUE;
else if (driveValue < MIN_DRIVE_VALUE)
driveValue = MIN_DRIVE_VALUE;
/* Save the motor drive value for next time.
NB: This is where you write to the PWM hardware too */
motorPWMvalue = (byte)driveValue;
} // if speedError not stupid

## Slide 39: Controller Output: PWM Channel Duty Cycle
Period is fixed
Controller varies DUTY CYCLE
NB: special cases to drive at 0 or 100%

## Slide 40: When does the control law run?
On a constant time-base whenever the motors need to move
How fast a time-base?
  Fast enough to avoid aliasing
  Rule of thumb: 0.1x to 0.05x of the dominant plant time constant
Measure your system and find out
  Switch the motor from off to full-on and measure the rise time of the motor speed with the load you expect to see on the motor

## Slide 41: Tuning?

## Slide 42: Transient Response
Setpoint
Controlled Variable
Time
Settling Time (TS)
Overshoot
Steady-state Error
Rise Time (TR)
10%
90%
Brad Nelson

## Slide 43: To Tune Your Controller…
You’ll need be able to:
Enable/Disable the control law calculation
Change the setpoint (step change)
Try different controller gains
Read and record the value of servo variables
  Feedback speed from encoder
  Error
  Controller output
  Error integral

## Slide 44: Demo …
How to use FreeMaster to change variables and grab a plot of variables over time

## Slide 45: Implications for your SW design…
All controller-related gains should be in global variables so they can be changed in the debugger without recompiling (at least during tuning)
All calculated values should get saved to global variables so they can be tracked – even those you don’t need to keep around

## Slide 46: The Bottom Line…
Why control DC motor speed?
  To get the desired wheel speed so the robot goes where you want
How to drive motor?
  PWM module in HCS12
How to measure motor speed?
  Timer Input Capture (IC) in HCS12
Controller implementation
  Timer ISR (OC) in HCS12
PI controller
  Use Integer math!
  2 static variables – integral error & last controller output
Tune with FreeMaster to pick workable P- and I- gains

## Slide 47: Summary…
You need to home the stepper motor to know where the camera is pointing.
You need to control speed of both motors to move in a straight line or controlled arc.
The control law you need to write will calculate a new PWM value from the current setpoint and measured speed.
When connected into a negative feedback loop with both proportional and integral terms, 2 parameters need to be tuned.
FreeMaster is a tool that allows you to change parameters and visualize the operation of the controller to achieve acceptable performance.

## Slide 48
fin